## Slide 1: Stormwater Advisory Group Meeting #5
City Hall, Public Works Department, Traffic Control Conference Room
June 24, 2024

## Slide 2: Agenda
Welcome (5 min)
Meeting #4 Recap (10 min)
Proposed Code Amendments and Timeline (20 min)
Stormwater Design Standards and Timeline (20 min)
Future Subgroup Meetings for Stormwater Design Standards (10 min)
Closing Comments (5 min)

## Slide 3: Common Acronyms
DEQ | Department of Environmental Quality
FC | Flow Control
GSI | Green Stormwater Infrastructure
LID | Low Impact Development
MEF | Maximum Extent Feasible
MS4 | Municipal Separate Storm System
SF | Square Feet
SFR | Single-Family Residential
SRC | Salem Revised Code

## Slide 4: 1. Welcome

## Slide 5: 2. Meeting #4 Recap
Revised Defintions

## Slide 6: Recap: Appendix 4A and Site Assessment Checklist
Clarified Infiltration Infeasibility Criteria is based on vertical separation between the stormwater facility bottom and seasonal high groundwater.
Reflects use of Area Set Aside (10%) in cases where infiltration testing has not been completed.
Clarified submittal requirements based on Simplified, Engineered or Area Set Aside method.
  Area Set Aside does not require an assumed infiltration rate to check footprint area.
  As a conservative assumption, the designer could check facility footprint based on a design infiltration rate.
    0.5”/hr requires full infiltration of the water quality storm (assumed largest GSI footprint required unless GSI is also being used to meet flow control performance standard)
    Flow control facility may be above or below ground.

## Slide 7: Recap: Simplified Sizing Form
Adjusted Project Category definition for RES and Large projects to align with threshold designations and project defintions.
  Stormwater facilities for Residential Projects (1,300 to 4,999 square feet of new or
  replaced impervious surface) must be sized for water quality at a minimum.
  Stormwater facilities for Large Projects (5,000 square feet or greater new or replaced impervious surface) must be sized for water quality and flow control.
Added note referring to Section 4.6 of the Design Standards for facility-specific design criteria applicable to the Simplified Method sizing.

## Slide 8: Recap: SRC Revised Definitions
Proposed for SRC | Current in SRC 70
Design storm event means the storm event with specific characteristics, such as recurrence interval, duration, intensity, and volume, that is used to design stormwater facilities. | Design storm event means the size of the storm event used to calculate runoff volumes and peak rates of discharge when designing stormwater facilities. The design storm event is the total inches of rainfall, distributed during a 24-hour period using a standard synthetic rainfall distribution identified as Type I-A by the Natural Resources Conservation Service.
Flow Control Exemption Area means the area determined by the Director to have sufficient capacity to receive discharges of drainage water such that a site discharging to the area is not required to meet the flow control performance standards of SRC 71.095(c). | None.
Green stormwater infrastructure, GSI, means a stormwater facility that uses vegetation, soils, or natural processes to promote natural surface hydrologic functions through infiltration or evapotranspiration. Stormwater facilities designed for full infiltration (no underdrain) or partial infiltration (with underdrain) of drainage water are considered GSI. | Green stormwater infrastructure means a stormwater facility that mimics natural surface hydrologic functions through infiltration or evapotranspiration, or that involves stormwater reuse.
Impervious surface means an area or surface that retards saturation of direct rainfall or otherwise causes drainage water to run off the land surface at an increased rate of flow from that present under predeveloped conditions. Common impervious surfaces may include but are not limited to building roofs, concrete or asphalt paving on walkways, driveways, parking lots, gravel subject to vehicular traffic, roads, compacted soil, and compacted fill. | Impervious surface means any surface exposed to rainwater from which most water runs off.
Large project means a project including 5,000 square feet or more of new impervious surface, replaced impervious surface, or new pervious pavement, individually or combined, on private property; or a project including 5,000 square feet or more of new impervious surface, replaced impervious surface, or new pervious pavement, individually or combined, in public right-of-way. | Large project means a project including 10,000 square feet or more of new pervious surface, new impervious surface, or replaced impervious surface, individually or combined, on private property; or, a project including 10,000 square feet or more of new pervious surface, new impervious surface, or replaced impervious surface, individually or combined, in public right-of-way.

## Slide 9: Recap: SRC Revised Definitions
Proposed for SRC | Current in SRC 70
Maximum extent feasible, MEF, means the extent to which a requirement or performance standard must be complied with as constrained by the physical limitations of the site, while providing reasonable considerations to engineering design, financial costs, and environmental impacts. For compliance with SRC 71.100, MEF means using green stormwater infrastructure to meet performance standards for treatment (SRC 71.100(c)) by infiltrating and treating the water quality design storm. | Maximum extent feasible, MEF, means the extent to which a requirement or standard must be complied with as constrained by the physical limitations of the site, practical considerations of engineering design, and reasonable considerations of financial costs and environmental impacts.
New impervious surface means any impervious surface resulting from a project that 1) is placed over a previously pervious surface; 2) is placed or over a surface that previously was in a predeveloped state; or 3) is placed over an existing impervious surface that does not have a stormwater system. | None.
Pervious pavement means pervious concrete, porous asphalt, or permeable paver blocks that infiltrate drainage water. | None.
Pervious surface means a surface that does not meet the definition of impervious surface. By way of illustration but not limitation, pervious surfaces include landscaping, amended soils, uncompacted gravel, lawns, sand, and pervious pavement. | None.
Replaced impervious surface means the removal of an existing impervious surface and replacement with new impervious surface. Replacement Replaced impervious surface does not include repair or maintenance activities on structures, paved surfaces, or stormwater facilities taken to prevent decline, lapse, or cessation in the use of the existing impervious surfaces as long as no additional hydrologic impact results from the repair or maintenance activity. By way of illustration but not limitation, hydrologic impacts can include changes in the routing of drainage water flows, changes in drainage water flow rates, changes in the duration of drainage water flows, or changes in drainage water flow volumes (e.g., changes to the location, rate, or volume of stormwater runoff) from a given site. | Replaced impervious surface means the removal of impervious surface down to earth material and replacement with new impervious surface. Replacement does not include repair or maintenance activities on structures, paved surfaces, or facilities taken to prevent decline, lapse, or cessation in the use of the existing impervious surfaces as long as no additional hydrologic impact results from the repair or maintenance activity.

## Slide 10: 3. Proposed Stormwater Code Amendments

## Slide 11: Proposed Amendments SRC 70 - Definitions
  Cross-reference. Cross-reference one definition with another in SRC 70/Other SRC chapter.
  Examples: Construction activity, Contaminant, Development, Earth material, Erosion, and Single-family residential project.
  Alignment. Align the City’s definition with the Municipal Stormwater Permit.
  Examples: Green stormwater infrastructure, Impervious surface, Numeric stormwater retention requirements, Pollutant, and Water quality design storm.
  Compliance. Amend to comply with Municipal Stormwater Permit.
  Examples: Large project, Maximum extent feasible, Replaced impervious surface.
  Addition. New definitions to clarify and better codify existing practice.
  Examples: Flow control exemption area, new impervious surface, Pervious pavement, pervious surface, Residential project.

## Slide 12: Proposed Amendments SRC 71
  SRC 71.025 (Fee-in-lieu of construction). Provides for opportunity of using a fee-in-lieu to not only construct new but to also retrofit an existing stormwater facility.
  SRC 71.055 (Permissible Discharges). Aligns the set of permissible discharges in code with those of the Municipal Stormwater Permit.
  SRC 71.080 (Requirements for land divisions). Clarifies that land divisions must be provided with both flow control and treatment facilities. Establishes the date at which the new requirements will apply to land divisions.
  SRC 71.085 (Requirements for residential projects).
  Accounts for recent changes in zoning and development codes to incorporate middle housing.
  SRC 71.087 (Requirements for City projects).
  Establish the date beyond which the new provisions apply to City projects.

## Slide 13: Proposed Amendments SRC 71
  SRC 71.090 (Requirements for large projects). Incorporates requirement in Municipal Stormwater Permit specific to provide stormwater treatment using GSI to the maximum extent feasible.
  SRC 71.095 (Flow control facilities). Add to “applicability” an exemption for projects discharging directly into a “flow control exemption area” as newly defined in SRC 70.005. Clarifies the flow control performance standards.
  SRC 71.100 (Treatment facilities).
  As required by the Municipal Stormwater Permit, states that the water quality design storm must be retained.

## Slide 14: Timeline for Amending SRC 70 & SRC 71
Jun 18 Staff Report “In Approval Tracking” in Legistar for 1st Reading
Jul 08 City Council meeting – First Reading and refer to Planning Commission
Jul 15 35-day DLCD Notice (for Aug 20 public hearing)
Jul 31 20-day Measure 56/SRC 300.1110 Notice (for Aug 20 public hearing)
Aug 20 Planning Commission meeting – Public Hearing
Sep 4 Staff Report “In Approval Tracking” in Legistar for 2nd Reading
Sept 23 City Council meeting – Second Reading (Start of land use appeal period)
Oct 28 30-day appeal period ends on Code Amendments
Nov 01 SRC Chapter 70, SRC Chapter 71, PWDS Effective

## Slide 15: Timeline for Amending Admin Rule
Aug 19 Finalize PWDS Admin Rule for Notice
Aug 20 Planning Commission meeting – Public Hearing
Aug 27 Issue Notice of Rulemaking (15-day minimum notification)
Sept 10 End of Notification Period for Rulemaking (Compile Comments)
Sept 23 City Council meeting – Second Reading (Start of land use appeal period)
Sept 25 Info Staff Report on Rulemaking “In Approval Tracking” in Legister
Oct 14 City Council meeting – Information Staff Report on Rulemaking
Nov 01 SRC Chapter 70, SRC Chapter 71, PWDS Effective

## Slide 16: 4. Design Standards Update

## Slide 17: Recap: Stormwater Design Standards - Revised Definitions
Proposed for Standards | Rationale
Drainage Water – Stormwater, groundwater, surface drainage, subsurface drainage, spring water, well overflow, roof drainage, or other like drainage other than sewage or industrial waste. | New definition. Used in lieu of “stormwater” to exclusively reference water managed with stormwater facilities.
Filtration Facility – A stormwater facility designed to exclusively treat stormwater runoff by filtration through media. A filtration facility does not promote infiltration and may be lined. | New definition. Helps define facility type in conjunction with performance standards and infiltration prioritization.
Flow Control Facility – A stormwater facility designed to control the flow rate, flow volume, or flow duration of drainage water. | Used instead of “detention facility” to identify stormwater facilities meeting the flow control performance standard.
All updated definitions per SRC incorporated into Design Standards.
Additional definitions listed below.

## Slide 18: Recap: Stormwater Design Standards - Revised Definitions
Proposed for Standards | Rationale
Infiltration Facility - a stormwater facility designed without a liner or underdrain to treat and fully infiltrate a design storm event. | New definition. Helps define facility type in conjunction with performance standards and infiltration prioritization.
Low Impact Development (LID) - a comprehensive land planning and engineering design approach to stormwater management with a goal of mimicking the pre-development hydrologic regime of urban and developing watersheds. | Interpreted from NPDES permit. Use to reference updated site planning requirements.
Partial Infiltration Facility - a stormwater facility design without a liner but with an underdrain to treat and promote infiltration of a design storm event. | New definition. Helps define facility type in conjunction with performance standards and infiltration prioritization.
Predeveloped - The conditions on a site in its natural, or undeveloped state, generally characterized by a mixture of trees, brush, weeds, and grass, and which is used to determine the allowable post-development discharge peak rates and flow volumes. The runoff characteristics for calculating allowable outflow are based on the combination of woods and grasslands (see calculated curve numbers in Appendix 4D). | References design assumptions more directly and City’s approach to addressing hydromodification impacts.
Project – Ground disturbing activity, the addition the addition of new impervious surface; the addition of new pervious pavement; or the replacement of impervious surface. | Confirms design activities that would trigger Design Standards.

## Slide 19: Recap: Stormwater Design Standards - Revised Definitions
Proposed for Standards | Current in the Standards
Stormwater Facility―A facility designed to control the flow rate, flow volume, or flow duration of drainage water, or a facility designed to remove pollutants from drainage water. | Added for consistency with SRC.
Stormwater System – All stormwater facilities and improvements such as catch basins, curbs, culverts, gutters, ditches, manmade channels, and storm drains that collect, convey, or control the flow of stormwater or remove pollutants from drainage water. | Added for consistency with SRC.
Water Quality Design Storm Event – a design storm event representative of 80% of the average annual runoff and is used to size stormwater facilities for water quality treatment. | Updated for consistency with the NPDES permit.

## Slide 20: Organization and New Sections
Section 4.1: Introduction
  Inclusion of Exemptions as a new section (4.1(d))
  Align How to Use these Standards with reorganization.
Section 4.2: Project Thresholds
  Remove Non-SFR as a category.
  Update SFR to RES and include new thresholds.
Section 4.3: Site Assessment and Planning
  Reference of Site Assessment and Planning Checklist (4.3(a))
  Introduce Infiltration Feasibility upfront
  Summarize Infiltration Testing Requirements
  Clarify Impervious Area Reduction Techniques and application for treatment or flow control facility sizing.

## Slide 21: Outstanding Question
Should use of Green Roofs be allowed credit for flow control sizing?

## Slide 22: Organization and New Sections
Section 4.4: General Design Requirements
  Inclusion of “Prioritize Infiltration” instead of a GSI to the MEF.
  Added section for Design Exceptions and Fee-in-lieu to reflect submittal of Appendix 4E equivalent.
Section 4.5: Performance Standards and Design Methodologies
  Add design storm table
  Clarify water quality (with NSRR) and flow control performance standards
  Consolidate sizing methods to one section: Simplified and Engineered.
  Engineered Sizing Calculations include Volume-based sizing and Hydrograph- based Sizing
Section 4.6: Design Criteria for Treatment and Flow Control
  Provide description and detail reference for facilities upfront
  Organized by GSI facilities, filtration facilities, and flow control facilities
  Incorporate applicable design criteria from standard details.

## Slide 23: Outstanding Questions
Where are clarification needs related to Sizing Calculations (approved tools, methods, etc)?
Should Simplified Method be used for public facilities?

## Slide 24: Stormwater Facilities
Stormwater Facility Type | GSI Facility1 | Filtration Facility2 | Design for Flow Control | Private Application Only
Section 4.6(b)(1) - Planters |  |  |  | 
Infiltration Planters | X |  | X | 
Partial Infiltration Planters | X |  | X | 
Lined Planters |  | X | X | 
Section 4.6(b)(2) - Rain Gardens |  |  |  | 
Infiltration Rain Garden | X |  | X | 
Partial Infiltration Rain Garden | X |  | X | 
Lined Rain Garden |  | X | X | 
Section 4.6(b)(3) - Flow Dispersion | X |  | X | 
Section 4.6(b)(4) – Subsurface Infiltration |  |  |  | 
Soakage Trench | X |  | X | 
Leach Line | X |  | N/A | X
Drywells | X |  | X | X
Manufactured Chamber Technology | X |  | X | X
Section 4.6(b)(5) - Pervious Pavement3 | X |  | X | X
Section 4.6(b)(6) - Green Roofs3 | X |  |  | 
Section 4.6(b)(7) - Constructed Wetland Treatment Systems |  |  |  | 
Treatment Wetland | X |  | X | 
Subsurface Gravel Wetland | X |  | X | 
Section 4.6(c)(1) - Vegetated Swales |  | X |  | 
Section 4.6(c)(2) - Vegetated Filter Strips |  | X |  | 
Section 4.6(c)(3) - Manufactured Treatment Technology |  | X |  | X
Section 4.6(d)(1) - Dry Ponds |  |  | X | 
Section 4.6(d)(2) - Structural Flow Control Facilities |  |  | X | 

## Slide 25: Organization and New Sections
Section 4.7: Planting and Landscape Requirements
  No change
Section 4.8: Operations and Maintenance
  No change
Section 4.9: Conveyance Systems
  Reflect rational method for use in calculating flow subject to pipe sizing

## Slide 26: Appendices
Appendix 4A: Stormwater Submittal Requirements
  Includes Site Assessment Checklist and Simplified Sizing Form
Appendix 4B: Landscape Requirements and Plant Lists for Stormwater Facilities
  Updated plant lists per Stakeholder feedback
Appendix 4D: Hydrologic Analysis
  Minor updates to sizing criteria
Appendix 4E: Design Exceptions and Fee in Lieu
  Updated Content
Appendix 4F: Accepted Manufactured Facilities
  Refine Contech StormFilter flow rates

## Slide 27: Thank you.
Any questions?